## Slide 1: Fibre Optics
by
Dr. Kamalpreet Kaur

## Slide 2
Optical Fibre
Optical Fibre is an optical transmission device which works on the principle of total internal reflection.
When a light signal is directed at one end of the fibre at a suitable angle, it undergoes repeated total internal reflection along the length of the fibre and finally comes out at the other end.
Principle of Optical Fibre

## Slide 3: Optical Fiber
Core
  Glass or plastic with a higher index of refraction than the cladding
  Carries the signal
Cladding
  Glass or plastic with a lower index of refraction than the core
Buffer
  Protects the fiber from damage and moisture
Jacket
  Holds one or more fibers in a cable

## Slide 6
Potential low cost: The glass which generally provides the optical fiber transmission medium is made from sand (SiO2).
Using an Optical fiber, 15000 independent speeches can be sent where as using a pair of copper wires, only 48 independent speeches can be sent
Enormous band width: The optical carrier frequency in the range 1013 to 1016 Hz.
In metallic cable systems band width is 500-700 MHz's. The amount of data that can be transmitted in a fixed amount of time.
Signal security: Optical fibers provides the high degree of signal security.

## Slide 7
Types of Optical Fibre (Based on core size)
Single Mode / Monomode Fibre
Multimode Fibre
Multimode
Step Index Fibres
Multimode
Graded Index Fibres

## Slide 8: Single Mode Step Index Fiber
Single mode step index fiber has a core diameter of 8 to 9 microns, which only allows one light path or mode
Index of refraction
Single mode fibres have a lower signal loss and a higher information capacity or bandwidth than a multimode fibre.

## Slide 9: Multimode Step-Index Fiber
Multimode fiber has a core diameter of 50 to 100 microns (sometimes even larger)
  Allows several light paths (~100) or modes
  This causes modal dispersion – some modes take longer to pass through the fiber than others because they travel a longer distance
Index of refraction

## Slide 10: Multimode Graded-Index Fiber
The index of refraction gradually changes across the core
  Modes that travel further also move faster
  This reduces modal dispersion so the bandwidth is greatly increased
Index of refraction

## Slide 11: Step-index and Graded-index
Step index multimode was developed first, but rare today because it has a low bandwidth (50 MHz-km)
It has been replaced by graded-index multimode with a bandwidth up to 2 GHz-km

## Slide 12: Fiber Optic Specifications
Attenuation
  Loss of signal, measured in dB/km
Dispersion
  Blurring of a signal, affects bandwidth
Bandwidth
  The number of bits per second that can be sent through a data link
Acceptance angle
  Measures the largest angle of light that can be accepted into the core

## Slide 13: Acceptance Angle
Optical fibre will only propagate light that enters the fibre within a certain cone, known as acceptance cone of the fibre. The half-angle of this cone is called the acceptance angle (θi)
From Snell’s law

## Slide 14
If i increases, Φ increases and θ decreases.
There is a maximum value of i beyond which the light ray entering the fibre will fall on the core-cladding interface at an angle less than θc. Such a ray will be refracted into the cladding and will not propagate. This maximum value of i, say imax is called the acceptance angle of the fibre.

## Slide 15
When then according to Snell’s law

## Slide 16
Taking for air, we get
This equation gives a relation between the acceptance angle and the refractive indices of the core and the cladding.
The cone associated with the angle imax is called the acceptance cone.

## Slide 17: Numerical Aperture
It is the measure of the light gathering capacity of the fibre and is defined as the product of sine of the acceptance angle and the refractive index of the medium to which the end faces of the fibre are exposed.
Taking for air, we get
Relative index

## Slide 18
V Number
The number of modes of multimode fiber cable depends on the wavelength of light, core diameter and material composition. This can be determined by the Normalized frequency parameter (V) or mode volume no.
Where , r = radius of fiber core;
λ = wavelength of light
NA=numerical aperture
For Step-index
For Graded-index
Mathematically, the number of modes for a fiber is given by:

## Slide 19: Cut off wavelength
NOTE:
1. For a single mode fiber, V < 2.405
2. For multimode fiber, V > 2.405
3. Cut off wavelength is wavelength corresponding to V=2.405

## Slide 20
ATTENUATION
Attenuation or transmission loss is the loss of optical power as light travels down a fiber. It is due to impurities in glass fiber or due to absorption of fiber.
The decrease in signal strength along a fiber optic waveguide caused by absorption and scattering is known as attenuation.
Attenuation cofficient is usually expressed in dB/km
Since attenuation is the loss, therefore, it is always expressed as
where α is the attenuation coefficient of the fiber

## Slide 21
The General Communication System

## Slide 22
The Optical fibre Communication System

## Slide 23
THE OPTICAL FIBER COMMUNICATION SYSTEM

## Slide 24
Dispersion
Dispersion, expressed in terms of the symbol ∆t, is defined as pulse spreading in an optical fibre.
As a pulse of light propagates through a fibre, elements such as numerical aperture, core diameter, refractive index profile, wavelength, and laser line width cause the pulse to broaden. This poses a limitation on the overall bandwidth of the fibre.

## Slide 25: Dispersion is of two types:
Internal dispersion/modal dispersion
Intramodal dispersion

## Slide 26: Modal Dispersion
Modal Dispersion
  Spreading of a pulse because different modes (paths) through the fiber take different times
  Only happens in multimode fiber
  Reduced, but not eliminated, with graded-index fiber

## Slide 27: Intramodal dispersion
It takes place even if only one mode is allowed to propagate in the optical fibre and takes place due to following effects:
Material dispersion
Due to the different time taken by different wavelengths to cross the optical fibre if the source is not monochromatic.
(2) Waveguide dispersion
A small portion of light reaches to the output end of fibre through cladding. As refractive index of cladding is less than core, so light through cladding will travel faster. At output end make the pulse broaden at output end.

## Slide 29
Coupling Losses
Loss splice (or fuse) < 0.02 dB
Loss connector ± 0.5 dB