## Slide 1: Unit IV
Network Overview- topologies, Switching and routing concepts, Firewalls, VLANs, Cryptography & PKI basics, Identity & Access Managements, Storage Security , Network Security (Firewalls, IDS/IPS),
Server Security configuration Control & patch management, Firewalls, Virtualization Security.

## Slide 2: Bus Topology
Bus topology is a network type in which every computer and network device is connected to single cable. When it has exactly two endpoints, then it is called Linear Bus topology.

## Slide 3: Features of Bus Topology
It transmits data only in one direction.
Every device is connected to a single cable
Advantages of Bus Topology
It is cost effective.
Cable required is least compared to other network topology.
Used in small networks.
It is easy to understand.
Easy to expand joining two cables together.

## Slide 4: Disadvantages of Bus Topology
Cables fails then whole network fails.
If network traffic is heavy or nodes are more the performance of the network decreases.
Cable has a limited length.
It is slower than the ring topology.

## Slide 5: Ring Topology
It is called ring topology because it forms a ring as each computer is connected to another computer, with the last one connected to the first. Exactly two neighbours for each device.

## Slide 6: Features of Ring Topology
A number of repeaters are used for Ring topology with large number of nodes, because if someone wants to send some data to the last node in the ring topology with 100 nodes, then the data will have to pass through 99 nodes to reach the 100th node. Hence to prevent data loss repeaters are used in the network.
The transmission is unidirectional, but it can be made bidirectional by having 2 connections between each Network Node, it is called Dual Ring Topology.
In Dual Ring Topology, two ring networks are formed, and data flow is in opposite direction in them. Also, if one ring fails, the second ring can act as a backup, to keep the network up.
Data is transferred in a sequential manner that is bit by bit. Data transmitted, has to pass through each node of the network, till the destination node.

## Slide 7: Advantages of Ring Topology
Transmitting network is not affected by high traffic or by adding more nodes, as only the nodes having tokens can transmit data.
Cheap to install and expand

## Slide 8: Disadvantages of Ring Topology
Troubleshooting is difficult in ring topology.
Adding or deleting the computers disturbs the network activity.
Failure of one computer disturbs the whole network.

## Slide 9: STAR Topology
In this type of topology all the computers are connected to a single hub through a cable. This hub is the central node and all others nodes are connected to the central node.

## Slide 10: Features of Star Topology
Every node has its own dedicated connection to the hub.
Hub acts as a repeater for data flow.
Can be used with twisted pair, Optical Fibre or coaxial cable.

## Slide 11: Advantages of Star Topology
Fast performance with few nodes and low network traffic.
Hub can be upgraded easily.
Easy to troubleshoot.
Easy to setup and modify.
Only that node is affected which has failed, rest of the nodes can work smoothly.

## Slide 12: Disadvantages of Star Topology
Cost of installation is high.
Expensive to use.
If the hub fails then the whole network is stopped because all the nodes depend on the hub.
Performance is based on the hub that is it depends on its capacity

## Slide 13: MESH Topology: Routing
In routing, the nodes have a routing logic, as per the network requirements. Like routing logic to direct the data to reach the destination using the shortest distance. Or, routing logic which has information about the broken links, and it avoids those node etc. We can even have routing logic, to re-configure the failed nodes.

## Slide 14: MESH Topology: Flooding
In flooding, the same data is transmitted to all the network nodes, hence no routing logic is required. The network is robust, and the its very unlikely to lose the data. But it leads to unwanted load over the network.

## Slide 15: Types of Mesh Topology
Partial Mesh Topology : In this topology some of the systems are connected in the same fashion as mesh topology but some devices are only connected to two or three devices.
Full Mesh Topology : Each and every nodes or devices are connected to each other.

## Slide 16: Features of Mesh Topology
Fully connected.
Robust.
Not flexible.

## Slide 17: Advantages of Mesh Topology
Each connection can carry its own data load.
It is robust.
Fault is diagnosed easily.
Provides security and privacy.

## Slide 18: Disadvantages of Mesh Topology
Installation and configuration is difficult.
Cabling cost is more.
Bulk wiring is required

## Slide 19: TREE Topology
It has a root node and all other nodes are connected to it forming a hierarchy. It is also called hierarchical topology. It should at least have three levels to the hierarchy.

## Slide 20: Features of Tree Topology
Ideal if workstations are located in groups.
Used in Wide Area Network.

## Slide 21: Advantages of Tree Topology
Extension of bus and star topologies.
Expansion of nodes is possible and easy.
Easily managed and maintained.
Error detection is easily done.

## Slide 22: Disadvantages of Tree Topology
Heavily cabled.
Costly.
If more nodes are added maintenance is difficult.
Central hub fails, network fails.

## Slide 23: HYBRID Topology
It is two different types of topologies which is a mixture of two or more topologies. For example if in an office in one department ring topology is used and in another star topology is used, connecting these topologies will result in Hybrid Topology (ring topology and star topology).

## Slide 24
Features of Hybrid Topology
It is a combination of two or topologies
Inherits the advantages and disadvantages of the topologies included
Advantages of Hybrid Topology
Reliable as Error detecting and trouble shooting is easy.
Effective.
Scalable as size can be increased easily.
Flexible.

## Slide 25: Disadvantages of Hybrid Topology
Complex in design.
Costly.

## Slide 26: Switching and Routing Concepts
Repeater – A repeater operates at the physical layer. Its job is to regenerate the signal over the same network before the signal becomes too weak or corrupted so as to extend the length to which the signal can be transmitted over the same network. An important point to be noted about repeaters is that they do not amplify the signal. When the signal becomes weak, they copy the signal bit by bit and regenerate it at the original strength. It is a 2 port device.

## Slide 27
Hub – A hub is basically a multiport repeater. A hub connects multiple wires coming from different branches, for example, the connector in star topology which connects different stations. Hubs cannot filter data, so data packets are sent to all connected devices. In other words, collision domain of all hosts connected through Hub remains one. Also, they do not have intelligence to find out best path for data packets which leads to inefficiencies and wastage.

## Slide 28: BRIDGE
Bridge – A bridge operates at data link layer. A bridge is a repeater, with add on functionality of filtering content by reading the MAC addresses of source and destination. It is also used for interconnecting two LANs working on the same protocol. It has a single input and single output port, thus making it a 2 port device.

## Slide 29: Bridges
Switch – A switch is a multi port bridge with a buffer and a design that can boost its efficiency(large number of ports imply less traffic) and performance. Switch is data link layer device. Switch can perform error checking before forwarding data, that makes it very efficient as it does not forward packets that have errors and forward good packets selectively to correct port only. In other words, switch divides collision domain of hosts, but broadcast domain remains same.

## Slide 30: Router
Routers – A router is a device like a switch that routes data packets based on their IP addresses. Router is mainly a Network Layer device. Routers normally connect LANs and WANs together and have a dynamically updating routing table based on which they make decisions on routing the data packets. Router divide broadcast domains of hosts connected through it.

## Slide 31: Gateway
Gateway – A gateway, as the name suggests, is a passage to connect two networks together that may work upon different networking models. They basically works as the messenger agents that take data from one system, interpret it, and transfer it to another system. Gateways are also called protocol converters and can operate at any network layer. Gateways are generally more complex than switch or router.

## Slide 32: Differences

## Slide 33: Firewall
A firewall is a network security device that monitors incoming and outgoing network traffic and decides whether to allow or block specific traffic based on a defined set of security rules.
Firewalls have been a first line of defense in network security for over 25 years. They establish a barrier between secured and controlled internal networks that can be trusted and untrusted outside networks, such as the Internet.
A firewall can be hardware, software, or both.

## Slide 34: Proxy firewall
An early type of firewall device, a proxy firewall serves as the gateway from one network to another for a specific application. Proxy servers can provide additional functionality such as content caching and security by preventing direct connections from outside the network. However, this also may impact throughput capabilities and the applications they can support.

## Slide 35: Stateful inspection firewall
Now thought of as a “traditional” firewall, a stateful inspection firewall allows or blocks traffic based on state, port, and protocol. It monitors all activity from the opening of a connection until it is closed. Filtering decisions are made based on both administrator-defined rules as well as context, which refers to using information from previous connections and packets belonging to the same connection.

## Slide 36: Unified threat management (UTM) firewall
A UTM device typically combines, in a loosely coupled way, the functions of a stateful inspection firewall with intrusion prevention and antivirus. It may also include additional services and often cloud management. UTMs focus on simplicity and ease of use.

## Slide 37: Next-generation firewall (NGFW)
Firewalls have evolved beyond simple packet filtering and stateful inspection. Most companies are deploying next-generation firewalls to block modern threats such as advanced malware and application-layer attacks.
According to Gartner, Inc.’s definition, a next-generation firewall must include:
Standard firewall capabilities like stateful inspection
Integrated intrusion prevention
Application awareness and control to see and block risky apps
Upgrade paths to include future information feeds
Techniques to address evolving security threats
While these capabilities are increasingly becoming the standard for most companies, NGFWs can do more.

## Slide 38: Threat-focused NGFW
These firewalls include all the capabilities of a traditional NGFW and also provide advanced threat detection and remediation. With a threat-focused NGFW you can:
Know which assets are most at risk with complete context awareness
Quickly react to attacks with intelligent security automation that sets policies and hardens your defenses dynamically
Better detect evasive or suspicious activity with network and endpoint event correlation
Greatly decrease the time from detection to cleanup with retrospective security that continuously monitors for suspicious activity and behavior even after initial inspection
Ease administration and reduce complexity with unified policies that protect across the entire attack continuum

## Slide 39: VLANs
A VLAN allows several networks to work virtually as one LAN. One of the most beneficial elements of a VLAN is that it removes latency in the network, which saves network resources and increases network efficiency.
In addition, VLANs are created to provide segmentation and assist in issues like security, network management and scalability. Traffic patterns can also easily be controlled by using VLANs.

## Slide 40: The key benefits of implementing VLANs include:
Allowing network administrators to apply additional security to network communication
Making expansion and relocation of a network or a network device easier
Providing flexibility because administrators are able to configure in a centralized environment while the devices might be located in different geographical locations
Decreasing the latency and traffic load on the network and the network devices, offering increased performance

## Slide 41: VLANs also have some disadvantages and limitations as listed below:
High risk of virus issues because one infected system may spread a virus through the whole logical network
Equipment limitations in very large networks because additional routers might be needed to control the workload
More effective at controlling latency than a WAN, but less efficient than a LAN

## Slide 42: Cryptography and PKI
The most distinct feature of Public Key Infrastructure (PKI) is that it uses a pair of keys to achieve the underlying security service. The key pair comprises of private key and public key.
Since the public keys are in open domain, they are likely to be abused. It is, thus, necessary to establish and maintain some kind of trusted infrastructure to manage these keys.

## Slide 43: Key Management
It goes without saying that the security of any cryptosystem depends upon how securely its keys are managed. Without secure procedures for the handling of cryptographic keys, the benefits of the use of strong cryptographic schemes are potentially lost.
It is observed that cryptographic schemes are rarely compromised through weaknesses in their design. However, they are often compromised through poor key management.
There are some important aspects of key management which are as follows −
Cryptographic keys are nothing but special pieces of data. Key management refers to the secure administration of cryptographic keys.
Key management deals with entire key lifecycle as depicted in the following illustration −

## Slide 44: There are two specific requirements of key management for public key cryptography.
Secrecy of private keys. Throughout the key lifecycle, secret keys must remain secret from all parties except those who are owner and are authorized to use them.
Assurance of public keys. In public key cryptography, the public keys are in open domain and seen as public pieces of data. By default there are no assurances of whether a public key is correct, with whom it can be associated, or what it can be used for. Thus key management of public keys needs to focus much more explicitly on assurance of purpose of public keys.

## Slide 45: Public Key Infrastructure (PKI)
PKI provides assurance of public key. It provides the identification of public keys and their distribution. An anatomy of PKI comprises of the following components.
Public Key Certificate, commonly referred to as ‘digital certificate’.
Private Key tokens.
Certification Authority.
Registration Authority.
Certificate Management System.

## Slide 46: Cryptography
The word cryptography in Greek means “secret writing.” The term today refers to the science and art of transforming messages to make them secure and immune to attacks.

## Slide 47: Key Encryption
Key: random string of characters.
• Weaves key into original data’s bits to generate unique data block.
– Cipher text.
– Longer keys make it more difficult to decrypt.
– Hackers may attempt to crack a key by using brute force attack.
• Keys randomly generated by encryption software.

## Slide 48: Private Key Encryption
Private key encryption is the form of encryption where only a single private key can encrypt and decrypt information.
It is a fast process since it uses a single key. However, protecting one key creates a key management issue when everyone is using private keys.
The private key may be stolen or leaked. Key management requires prevention of these risks and necessitates changing the encryption key often, and appropriately distributing the key.

## Slide 49: Private Key Encryption
c

## Slide 50: Public Key Encryption
Data encrypted using two keys:
  Private key.
  Public key associated with user.
Public key server: publicly accessible host that freely provides list of users’ public keys.
Key pair: combination of public key/private key.
Public keys more vulnerable than private keys
  Use longer keys.
  RSA: most popular public key algorithm.
Digital certificate: password-protected, encrypted file that holds identification information.

## Slide 51: Public Key Encryption

## Slide 52: Network Security
Intrusion Detection System
Intrusion Prevention System
Configuration management (CM)
Patch Management
Security operation center
Physical security
Virtualization Managament

## Slide 53: Patch Management
Patch management is the process that helps acquire, test and install multiple patches (code changes) on existing applications and software tools on a computer, enabling systems to stay updated on existing patches and determining which patches are the appropriate ones. Managing patches thus becomes easy and simple.
Patch Management is mostly done by software companies as part of their internal efforts to fix problems with the different versions of software programs and also to help analyze existing software programs and detect any potential lack of security features or other upgrades.
Software patches help fix those problems that exist and are noticed only after the software's initial release. Patches mostly concern security while there are some patches that concern the specific functionality of programs as well.

## Slide 55: Virtualization Security
Virtualization security is the collective measures, procedures and processes that ensure the protection of a virtualization infrastructure / environment.
It addresses the security issues faced by the components of a virtualization environment and methods through which it can be mitigated or prevented.

## Slide 56
Virtualization security is a broad concept that includes a number of different methods to evaluate, implement, monitor and manage security within a virtualization infrastructure / environment.
Typically, virtualization security may include processes such as
Implementation of security controls and procedures granularly at each virtual machine.
Securing virtual machines, virtual network and other virtual appliance with attacks and vulnerabilities surfaced from the underlying physical device.
Ensuring control and authority over each virtual machine.
Creation and implementation of security policy across the infrastructure / environment